River temperature modelling: A review of process-based approaches and future directions
Stephen J. Dugdalea,⁎, David M. Hannaha, Iain A. Malcolmb

1- Basics of process-based water temperature models
Energy ﬂuxes to or from the river channel are ﬁrst calculated using an energy balance equation which describes the net energy gains or losses as a series of radiative, latent, sensible and advective heat exchanges:

H_total = H_sw + H_lw + H_e + H_s + H_bhf + H_a ` ` ` ` ` (1)

where Htotal represents the total energy available for transfer to or from the river channel,
Hsw is the net shortwave solar radiation ﬂux,
Hlw is the net longwave radiation ﬂux,
He is the net energy ﬂux due to evaporation or condensation (latent heat ﬂux),
Hs is the net energy gain or loss from convection or conduction (sensible heat ﬂux),
Hbhf represents heat ﬂuxes to or from the river bed,
Ha is the energy gained or lost from groundwater or tributary inﬂows
(all in Wm−2).

Typically, radiative ﬂuxes (net shortwave and longwave radiation) dominate the heat budget of most river environments (Caissie, 2006), with solar shortwave radiation generally being the largest heat source for a river or stream (Morin and Couillard, 1990; Webb and Zhang,1997, 2004).
Incident shortwave radiation (Hsw) from the sun is typically the largest source of energy for a river system (particularly during summer months; Webb and Zhang, 1997), although bankside objects such as vegetation and/or topography can reduce the amount of solar radiation received by the river through providing shade (e.g. Garner et al., 2014, 2017).
Longwave radiation (Hlw) (Dugdale, 2016) can be both a heat source and sink, with downwelling longwave radiation from clouds, the land surface and bankside vegetation contributing to heat gains, and upwelling radiation from the water surface driving energy losses from the stream (e.g. Benyahya et al., 2012).
Outgoing longwave radiation (Hlw) from the river channel represents a common heat sink, especially during night time or the winter months but incoming longwave energy from the atmosphere (and riparian vegetation) can mediate heat losses in certain circumstances (Benyahya et al., 2012; Hannah et al., 2008).

Energy at the air-water interface is also gained or lost through non-radiative means (latent and sensible heat ﬂuxes; Hannah and Garner, 2015).
Latent heat ﬂux (He) comprises energy lost (gained) by the stream during evaporation (condensation) as water moves from a higher to lower energy state (or vice versa).
Latent (evaporative) heat loss is a signiﬁcant energy sink at the river surface (Webb and Zhang, 1997, 2004), particularly in large or open rivers (Maheu et al., 2014; Caissie, 2016).
Sensible heat ﬂux (Hs) encompasses mainly convective exchange between the air and water surface depending upon temperature diﬀerences and atmospheric mixing (Webb and Zhang, 1999). The magnitude of energy lost or gained through sensible heat exchange is generally lower than radiative or latent ﬂuxes (Caissie, 2006). However, sensible heat ﬂuxes can nonetheless impose a non-negligible control on river temperature (e.g. Webb and Zhang, 1997), acting as both a heat sink in the winter and a heat source during summer months.

While generally smaller in magnitude than surface heat ﬂuxes (Sinokrot and Stefan, 1994; Evans et al., 1998), energy exchange at the streambed-water interface has been noted an important component of the energy balance in some studies, particularly in the winter (e.g. Webb and Zhang, 1997; Hannah et al., 2004; Leach and Moore, 2014). At the water-streambed interface, heat is principally exchanged through advective (Ha) and conductive (Hbhf) processes.
Advective heat (Ha) transfers from groundwater exﬁltration and hyporheic exchanges drive both river temperature warming and cooling (e.g. Hannah et al., 2009; Hébert et al., 2011). Because the temperature of groundwater is broadly stable over the year and the water column exhibits a sinusoidal annual cycle, streambed advective exchanges contribute to stream cooling in the summer and warming during winter months (Caissie, 2006).
Conduction (Hbhf) between the water column and streambed also drives heat exchange. These ﬂuxes generally act in the same direction as advective transfers, with heat being, lost from the water column to the (comparatively) cooler bed in the summer (Webb and Zhang, 2004).
However, radiative (shortwave (Hsw)) heating of the bed in in shallow streams can also drive positive conductive transfers from the bed to the water column (e.g. Evans et al.,
1998).

A ﬁnal source of energy at the water-streambed interface is ﬂuid friction between the water column and bed/banks. Friction gains are generally minor (e.g. Evans et al., 1998) and often considered negligible (Carrivick et al., 2012) for most rivers, but are sometimes observed in energetic environments (i.e. mountainous streams) with high roughness coeﬃcients (Brown and Hannah, 2008) or large bed material (Chikita et al., 2010).
Heat gains from ﬂuid friction can be a signiﬁcant source of heat in steeper streams with high roughness coeﬃcients (e.g. Hannah et al., 2004; Chikita et al., 2010; Khamis et al., 2015).

Once net heat ﬂux has been calculated, the river temperature change resulting from this energy gain (loss) is computed using Eq. (2).
The literature contains many variations on this equation (e.g. Sinokrot and Stefan, 1993; Rutherford et al., 1997; Tung et al., 2006; Hébert et al., 2011; Garner et al., 2014) which attempt to account for variability in discharge and channel morphology or compute heat transport in multiple dimensions. However, the basic one-dimensional heat advection-dispersion equation for an open channel of constant cross section and ﬂow is given by Sinokrot and Stefan (1993) :
{∂T_w} over {∂t} = - U{∂T_w} over {∂x} + D_L{∂T_w^{2}} over {∂x^{2}} + {H_total} over {ρ * c_p*d} ` ` ` ` ` (2)

where Tw is water temperature (°C) at time t,
U is mean channel velocity (ms−1),
x is streamwise distance (m),
DL is an empirically derived longitudinal dispersion coeﬃcient (ms−2),
ρ is the density of water (kgm−3),
cp is the speciﬁc heat of water (41.8 × 103 Jkg−1 °C−1),
d is the mean channel depth (m)

Provided that the channel is well mixed and does not contain notable lateral temperature gradients, the combination of Eqs. (1) and (2) can be used to simulate water temperature as a function of the input hydrometeorological and geomorphological data.
All process-based river temperature models use observed hydrometeorological data to calculate the energy ﬂuxes detailed in Eq. (1). the numerical representation of the physical energy ﬂuxes can vary substantially between diﬀerent river temperature models, and has implications for both model complexity and the quality of river temperature simulations.

2- Representation of fluxes
Incoming solar shortwave radiation
If observations of solar radiation (Hsw) are available for a given location, most models allow for the direct input of such data. Many process-based river temperature models contain complex routines capable of approximating the solar radiation received by a given point on the Earth's surface as a function of the date and time (see Boyd and Kasper, 2003 for appropriate algorithms). Because such algorithms yield predictions of solar radiation uninﬂuenced by the atmosphere, these models include further functions allowing for solar radiation values to be corrected for atmospheric transmissivity resulting from a range of factors (e.g. cloudcover, atmospheric dust/water vapour scattering, see Theurer et al.,1984 and Boyd and Kasper, 2003 for more detailed summary). Certain models even oﬀer the facility to use both observed solar radiation values and computed data.

Net longwave radiation
Some studies involving process-based river temperature models (e.g. Garner et al., 2014) incorporate observations of longwave radiation (Hlw) acquired from net radiometers, but such data are rarely available. all of the river temperature models summarised in Table1 oﬀer the ability to compute longwave radiative ﬂuxes as a function of other meteorological variables using a variant of the equation :

H_lw = H_(lw atm) - H_(lw stream) ` ` ` ` ` (3)

H_(lw atm) = (1 – R_L)* %epsilon_atm*%sigma*T_a ^4 ` ` ` ` ` (4) H_(lw stream) = %epsilon_w *%sigma* T_w^4 ` ` ` ` ` (5) given and

where εatm and εw (≈0.97) are the emissivity of the stream and the atmosphere respectively,
RL is the reﬂectance coeﬃcient of the stream surface (given as 1 − εw),
σ is the Stefan-Boltzmann constant (5.670367 × 10−8 Wm−2K−4),
Ta and Tw are the air and water temperature (°K) respectively

Complexities arise from the range of diﬀerent formulae available for the calculation of εatm. Most models calculate εatm as a function of either air temperature (Swinbank, 1963; Idso and Jackson, 1969) or vapour pressure (Brunt, 1932; Anderson, 1954) using simple empirically derived formulae, while others use the physically derived method of Brutsaert (1975) to compute εatm as a function of both air temperature and vapour pressure.
Some models even oﬀer multiple or composite methods for characterising εatm.
Additionally, because atmospheric emissivity is heavily inﬂuenced by cloud cover, a number of models oﬀer the ability to correct computed emissivity values for the eﬀect of cloud cover using the approach of Bolz (1949), something that is particularly useful in regions where cloudy/overcast conditions dominate.
Particular care should be taken when attempting to apply a river temperature model in environments with potential for a high proportion of longwave ﬂuxes (e.g. those with substantial tree/vegetation cover, or cloud-dominated meteorology); in such instances, it may be advisable to quantify incoming radiative energy (e.g. Hannah et al., 2008) using net radiometers.

Accounting for the eﬀects of riparian vegetation/topography on radiative ﬂuxes
It is necessary to account for the eﬀect of trees and topographic shading on radiative ﬂuxes when modelling stream temperature in such environments with near-stream vegetation and topography. While some models do not contain any mechanism to account for the eﬀect of vegetation/topography on radiation ﬂuxes, most incorporate algorithms that are able to simulate the reduction in solar shortwave radiation received by the stream.
Some models compute the eﬀects of shading using (amongst other variables) sun elevation, tree/topographic height and bank distance, canopy density and stream azimuth to compute a ‘shade factor’ coeﬃcient that represents the fraction of radiation that does not reach the stream surface due to shading. This coeﬃcient can then be applied to scale the solar radiation components of Eq. (1).
Other more complex algorithms function similarly, but partition incoming solar radiation into its direct and diﬀuse components. The direct solar radiation received at the stream surface is subsequently calculated either through application of the ‘shade factor’ coeﬃcient or through modelling the amount by which the solar ‘beam’ is attenuated as it travels through the tree canopy. The fraction of diﬀuse radiation received by the stream is then quantiﬁed separately, usually by means of an algorithm that computes the reach's sky view factor, a coeﬃcient that represents the fraction of the hemisphere that is unblocked by tree cover/topography. Most shading algorithms are directly integrated within their given stream temperature model. However, some models require that the shading correction be computed externally. Generally, these models rely on GIS analysis or similar to compute either the shade factor coeﬃcients or canopy transmissivity values which are then entered manually into the model. Although this additional step may mean that such models require more time to implement, the ability to manually enter shade correction values means that they are :
a) able to make use of advances in new shade correction algorithms
b) can be used with ﬁeld-derived values for shade correction (e.g. Rutherford et al., 1997) that do not rely on the application of an algorithm.

Some models also apply shading correction to longwave ﬂuxes. Atmospheric longwave radiation is aﬀected by riparian/topographic shading in much the same as the diﬀuse component of solar radiation ﬂux (Hannah et al., 2008). As such, the impact of shading on the atmospheric longwave ﬂux is generally calculated by computing a given reach's sky view factor (e.g. Cox and Bolte, 2007) and applying the resulting coeﬃcient to scale the longwave ﬂux given by Eq. (4).
Radiation from near-stream vegetation or topography can also represent a signiﬁcant source of longwave energy. Indeed, studies show that longwave radiation from tree cover can contribute signiﬁcantly to river temperature during nighttime (in comparison to open reaches; Benyahya et al., 2012; Hannah et al., 2008). As a result, the same models also contain routines that compute incident longwave radiation from riparian tree cover and/or topography. This allows such models to estimate longwave radiation ﬂuxes in tree-covered reaches with a high degree of accuracy, potentially improving their utility for predicting water temperature in steep headwater streams or heavily forested catchments.

An additional consideration concerns the spatial discretisation of the computed impacts of riparian vegetation on stream temperature. Because riparian vegetation can vary substantially along a river, any correction for riparian shading or longwave ﬂuxes must account for spatial variability in riparian vegetation. All of the models reviewed here contain routines capable of generating such spatially explicit data using either GIS polygons, tree height rasters or shading coeﬃcients as input data to correct radiative ﬂuxes at the scale of the model's structure (see Section 4.3). However, it is important that the chosen model's resolution is suﬃciently high to encapsulate true spatial variability in the impacts of riparian vegetation on stream temperature. Similarly, the riparian vegetation data provided to the model must be of a resolution equal to or better than that of the model itself. Recent studies have demonstrated the utility of LiDAR data for providing high resolution raster datasets of riparian vegetation height/shading (e.g. Wawrzyniak et al., 2017); such data are therefore particularly appropriate if attempting to model the ﬁne-scale (i.e. sub-reach) impacts of vegetation on stream temperature.

Latent and sensible heat ﬂuxes
Because direct measurements of energy gains or losses from latent or sensible heat ﬂuxes are rare (Maheu et al., 2014; Caissie, 2016), all of the river temperature models reviewed here derive net latent and sensible heat from meteorological observations.
The majority of equations for calculating latent heat ﬂuxes take the same initial form :
H_e = ρW*L_e* overline {E} ` ` ` ` ` (6)
where ρW is the density of water (1 × 10 kgm),
Le is the latent heat of vaporisation (2.5 × 106 Jkg−1),
Ē is the rate of evaporation (ms−1)

However, diﬀerences in computed latent heat ﬂuxes arise from the choice of equation used to compute Ē (Table 3). While some models currently oﬀer only relatively basic functionality for predicting evaporation rates as a function of air temperature and number of daylight hours (using the Thornthwaite, 1948 formula), the majority use a variation on Dalton's equation for evaporation (see Lim et al., 2012) to compute evaporation rates using wind speed, actual vapour pressure and saturation vapour pressure.
Most equations based around Dalton's equation involve some kind of empirical expression that estimates the adiabatic portion of evaporation as a function of wind speed and ﬁeld-derived coeﬃcients (referred to as the ‘wind function’, common coeﬃcients for which can be found in Boyd and Kasper, 2003 and Cole and Wells, 2015. The accuracy of eva- poration predictions can thus depend greatly upon the coeﬃcients used.
In an attempt to reduce the uncertainty associated with such empirical approaches, other models oﬀer the ability to use physically based equations (e.g. Penman, 1948; Monteith, 1965; Priestly and Taylor, 1972) that calculate evaporation rates based on a range of input hydrometeorological data (e.g. net irradiance, wind speed, saturation vapour pressure curve, aerodynamic conductance). The use of a model that incorporates a physically-based evaporation routine may be advisable when implementing a river temperature model in an environment for which ‘wind function’ coeﬃcients needed by Dalton-type approaches are unavailable. However, comparative studies present conﬂicting results regarding the relative accuracy of the various methods for computing evaporation (e.g. McJannet et al., 2013; Ouellet et al., 2014b; Alazard et al., 2015) meaning that is may not be advisable to apply these more complex routines unless evaporation rates predicted by simpler methods (e.g. Dalton's equation) are clearly erroneous.
Paragraphe bizarre
Conversely, while evaporative ﬂuxes are generally of greater magnitude in warmer climates, they can represent a highly signiﬁcant component of stream energy budgets in temperate regions (e.g. Hannah et al., 2008). It may therefore be advisable to measure the importance of evaporative ﬂux using an energy balance study (e.g. Hannah et al., 2008) or evaporation pan experiments (e.g. Maheu et al., 2014) prior to determining whether to apply a model with more complex routines for computing latent heat ﬂux.

All of the models reviewed here calculate sensible heat exchanges in essentially the same way following the method of Bowen (1926), either through multiplying the product of the wind function and the air-water temperature gradient by an empirical coeﬃcient, or by applying the Bowen ratio (itself a function of air and water temperature and vapour pressure) to the evaporative ﬂux. Consultation of the literature for the various temperature models documented here reveals minor discrepancies between the various sensible heat ﬂux equations and coefﬁcients used therein, largely resulting from either unit conversions and/or the necessity of accounting for diﬀerent wind function coeﬃcients. There is consequently little eﬀective diﬀerence in sensible heat ﬂux estimates yielded by the various models discussed here, meaning that model selection is generally driven by other (greater magnitude) sources of thermal energy (e.g. radiative, latent and advective ﬂuxes).

Heat ﬂuxes at the streambed interface
Some river temperature models do not incorporate routines capable of calculating bed heat ﬂux, considering its eﬀect on water temperature to be negligible. This is presumably because the majority of these models are designed for application in large river systems where the magnitude of heat exchanges at the streambed interface is particularly diminished in relation to other ﬂuxes (Caissie et al., 2014). However, many other models do incorporate bed heat ﬂuxes into their energy balance computations. This is generally accomplished using a variation on Fourier's Law (e.g. Story et al., 2003) whereby bed heat ﬂux is computed as a function of the streambed thermal gradient (change in temperature between the streambed-water interface and a given depth within the streambed; Theurer et al., 1984) multiplied by the bed thermal conductivity (the product of bed sediment density, bed heat capacity and bed thermal diﬀusivity; Boyd and Kasper, 2003). Most of these models refer to this equation as quantifying heat ﬂux arising from conduction between the bed and the water column. However, Hannah et al. (2004) note that it is extremely diﬃcult to disaggregate bed conduction, convection and advection when estimating bed heat ﬂux. Bed heat ﬂux computed with this method may therefore be considered a combination of these three energy exchanges.
As with other heat ﬂuxes detailed here, the quality of bed heat ﬂux predictions is reliant on input data quality and availability. Bed temperature gradient is generally measured using temperature loggers installed at given depths within the bed or modelled numerically given a priori knowledge of the bed material and temperature gradients within the riverbed (e.g. Sinokrot and Stefan, 1993), while thermal conductivity is governed by the type of bed material (i.e. lithology, porosity) and derived from laboratory analysis of bed sediments (data for which are often available in the literature; Hondzo and Stefan, 1994).
Observations of these parameters can be diﬃcult to ascertain, and it is often necessary to provide estimates to the temperature model. However, owing to the high degree of heterogeneity often present in bed temperatures (e.g. Birkel et al., 2016), obtaining even an average or estimate can be diﬃcult. In such circumstances, care must be taken to ensure that modelled bed heat ﬂuxes stay within realistic values. Furthermore, given the importance of conductive and advective (e.g. hyporheic-driven) bed heat ﬂuxes in some regions (e.g. Leach and Moore, 2014), the use of such ‘bulk’ approaches for computing bed heat ﬂuxes produces a highly simpliﬁed estimate of true bed energy transfer processes. Although recent research (e.g. Kurylyk et al., 2016; Caissie and Luce, 2017) has proposed improved methods for quantiﬁcation of bed heat ﬂuxes (and subsequent partitioning into their conductive, convective and advective components), these approaches have not yet been integrated into existing river temperature models and accurate modelling of bed heat ﬂuxes therefore remains a challenge.
In addition to the calculation of ‘bulk’ bed heat ﬂuxes, some models also include separate routines capable of estimating heat ﬂux due to solar heating of the bed. In most cases, river temperature models function under the assumption that the channel is deep enough that all solar radiation is attenuated within the water column. However, in certain circumstances (i.e. shallow headwater streams, streams with considerable exposed boulder material, very low turbidity environments; Chen et al., 1998a), solar warming of the streambed may contribute signiﬁcantly to river temperature warming (e.g. Evans et al., 1998; Clark et al., 1999; Webb and Zhang, 1999; Johnson, 2004). Because the magnitude of such heat ﬂuxes is both temporally or spatially variable (Webb and Zhang, 1997), it may be beneﬁcial to choose a model that accounts for these processes when modelling temperature in environments where radiative streambed warming is thought to occur. Where possible, it is therefore advisable to quantify the magnitude of bed heat ﬂuxes either by means of Fourier's law (e.g. Story et al., 2003) or by using soil heat ﬂux plates, in order to determine whether
a) the use of a model capable of accounting for bed heat ﬂuxes is necessary
b) the extent to which modelled ﬂuxes approximate observed data

Fluid friction with the bed and banks
Although only two publicly available models currently include routines for calculating ﬂuid friction, a range of studies have used the same simple equation for manually estimating friction-driven heat ﬂuxes (e.g. Marsh, 1990; Webb and Zhang, 1997; Hannah et al., 2004; Tung et al., 2006; Chikita et al., 2010; Cardenas et al., 2014). Should suspicions arise that the non-accounting for ﬂuid friction by a given model is biasing temperature estimates (e.g. in the case where the user is conﬁdent that all other heat ﬂux parameters are accurately modelled but temperature simulations still do not match observed data), it should at least be possible to estimate friction gains/losses outside of the model.
Furthermore, many coupled hydraulic-water temperature models already include routines for quantifying ﬂuid friction as part of their hydraulic computations. Given the ready ability to customise/script these models, it may be possible to devise routines which use the outputs of these computations to improve temperature estimates in high gradient streams. Nevertheless, with the exception of a few studies (e.g. Webb and Zhang, 1997, 1999) where ﬂuid friction was estimated to be high, such heat exchanges are generally assumed to be minor and can be considered negligible for the majority of temperature modelling scenarios (e.g. Carrivick et al., 2012; Johnson et al., 2014). The ability of a model to account for ﬂuid friction can therefore be considered a low priority during model selection, unless working in particularly high-energy environments.

Advective heat ﬂuxes
Inﬂows from tributaries or subsurface inputs can engender substantial temperature gradients in river systems (e.g. Torgersen et al., 1999; Torgersen et al., 2001). All of the models covered in this review contain routines capable of computing advective heat ﬂuxes using the same general equation:
T_(w,x) = {(T_(w,x−1) * Q) + (T_inflow * Q_inflow )} over {Q + Q_inflow} ` ` ` ` ` (7)

where Q and Qinflow are the discharge of the main channel and inﬂow respectively and Tinflow is the temperature of the inﬂow (Boyd and Kasper, 2003)
However, diﬀerences between the various models arise from :
a) the way in which boundary conditions are assigned to advective inputs,
b) the way in which inﬂows arriving from diﬀerent sources are disaggregated
c) the resolution at which inﬂows can be assigned within the model

In terms of assigning boundary conditions to advective inputs, the majority of temperature models require the user to manually input discharge and temperature data associated with inﬂows. These observations are relatively easy to obtain for surface inﬂows by means of temperature loggers and discharge gauges. Subsurface inputs are harder to quantify, given the scarcity of groundwater temperature records in many locations and the diﬃculty of quantifying groundwater ﬂux.
Groundwater temperature is therefore often assigned a value equal to mean annual air temperature given the close correlation between these two variables (e.g. Karanth, 1987). However, in regions where groundwater temperature departs signiﬁcantly from this trend, advective heat ﬂuxes resulting from groundwater inﬂows may be over- or under-represented. The need for ﬂow or temperature observations can be minimised by using coupled hydraulic or hydrological models (see Sections 4.1 and 4.2) which are able to estimate the ﬂows and temperatures associated with advective inputs. However, although these models are able to simulate surface water contributions with a reasonable degree of accuracy, the resolution of simulated groundwater inﬂows is often extremely course, requiring additional data on groundwater exﬁltration/temperature to be manually entered.

In terms of the disaggregation of inﬂows resulting from diﬀerent sources, some models discriminate between tributary inﬂows and those arising from groundwater processes, allowing tributary inﬂows to be assigned as point inputs, with groundwater inﬂows (or indeed, losses to the aquifer; Boyd and Kasper, 2003) modelled as diﬀuse inputs distributed along a given reach. Because inﬂows from diﬀerent subsurface zones (i.e. hyporheic vs. shallow ground water) have varying hydrologic characteristics (i.e. groundwater ﬂux generally involves a permanent change in water volume whereas hyporheic ﬂux is characterised by recurrent exchanges to and from the bed over shorter distances and time periods), some models even oﬀer the ability to model thermal inputs from diﬀerent subsurface zones (i.e. saturated vs unsaturated zones; hyporheic ﬂow). However, other models require input of ‘bulk’ inﬂows at discrete intervals within the model which merge surface and groundwater inputs together. This means that the true location of a given inﬂow may not be accurately represented within the model as the ‘merging’ of several inﬂows will require that their input location is also a reﬂection of their combined values. Because subsurface inﬂows are often more diﬀuse than tributaries, the merging of advective inputs in this manner may result in a river temperature response that is not properly representative of true subsurface or surface water mixing processes (Pike et al., 2013). Assigning temperatures to these combined inﬂow data can be diﬃcult given the likely temperature diﬀerence between surface and subsurface inﬂows owing to their diﬀerent thermal characteristics. In such instances, it may therefore be advisable to apply Eq. (6) to estimate the bulk temperature of the combined inﬂows before it is input into the model.
However, it should be noted that through merging diﬀuse and discrete advective inputs in this manner, a model may produce a false representation of the location and magnitude of warm or cool water inputs which may have implications for certain studies focusing on such phenomena (e.g. the ecological signiﬁcance of cool water refuges; Dugdale et al., 2016). The ability of a river temperature model to represent advective ﬂuxes is also dependent upon its resolution and structure (covered in further detail in Section 4.3). While less of an issue for models using a high resolution gridded structure whereby inﬂows can be assigned to each grid cell (allowing for multiple advective inputs in a relatively small spatial scale), models operating at reach scales only allow for inﬂows to be assigned at the resolution of nodes/segments. An appropriate segment resolution must be chosen in order to ensure that the river temperature response to local advective inputs is represented in the correct geographic location in order that modelled temperature accurate reﬂects observed data when conducting model calibration.

3- Model implementation
The diﬀerences between the available temperature models are not limited simply to their representation of physical energy ﬂuxes there is also substantial variability in the ways in which the various models are implemented. These diﬀerences lie in their ability to model hydraulic (i.e. ﬂow velocity and wetted cross-section) and/or hydrological (i.e. discharge or rainfall-runoﬀ) data, their structure (i.e. their spatio-temporal resolution and dimensionality), considerations regarding their calibration, and the degree to which the models are publicly available and/or open to customisation.

Hydraulic data

Liste des articles utilisés :
Alazard et al., 2015
Anderson, 1954
Benyahya et al., 2012
Birkel et al., 2016
Bolz (1949)
Bowen (1926)
Boyd and Kasper, 2003
Brown and Hannah, 2008
Brunt, 1932
Brutsaert (1975)
Caissie, 2006, 2014, 2016
Caissie and Luce, 2017
Carrivick et al., 2012
Cardenas et al., 2014
Chen et al., 1998a
Chikita et al., 2010
Chen et al., 1998a
Cole and Wells, 2015
Cox and Bolte, 2007
Dugdale et al., 2016
Dugdale, 2016
Evans et al., 1998
Garner et al., 2014, 2017
Hannah and Garner, 2015
Hannah et al., 2004, 2008, 2009
Hébert et al., 2011
Hondzo and Stefan, 1994
Idso and Jackson, 1969
Johnson, 2004
Karanth, 1987
Khamis et al., 2015
Kurylyk et al., 2016
Leach and Moore, 2014
Lim et al., 2012
Maheu et al., 2014
Marsh, 1990
McJannet et al., 2013
Monteith, 1965
Morin and Couillard, 1990
Ouellet et al., 2014b
Penman, 1948
Pike et al., 2013
Priestly and Taylor, 1972
Rutherford et al., 1997
Sinokrot and Stefan, 1993, 1994
Story et al., 2003
Swinbank, 1963
Theurer et al.,1984
Thornthwaite, 1948
Torgersen et al., 1999, 2001
Tung et al., 2006
Wawrzyniak et al., 2017
Webb and Zhang,1997, 1999, 2004