River temperature modelling: A review of process-based approaches and future directions
Stephen J. Dugdalea,⁎, David M. Hannaha, Iain A. Malcolmb

1- Basics of process-based water temperature models
Energy ﬂuxes to or from the river channel are ﬁrst calculated using an energy balance equation which describes the net energy gains or losses as a series of radiative, latent, sensible and advective heat exchanges:

H_total = H_sw + H_lw + H_e + H_s + H_bhf + H_a ` ` ` ` ` (1)

where Htotal represents the total energy available for transfer to or from the river channel,
Hsw is the net shortwave solar radiation ﬂux,
Hlw is the net longwave radiation ﬂux,
He is the net energy ﬂux due to evaporation or condensation (latent heat ﬂux),
Hs is the net energy gain or loss from convection or conduction (sensible heat ﬂux),
Hbhf represents heat ﬂuxes to or from the river bed,
Ha is the energy gained or lost from groundwater or tributary inﬂows
(all in Wm−2).

Typically, radiative ﬂuxes (net shortwave and longwave radiation) dominate the heat budget of most river environments (Caissie, 2006), with solar shortwave radiation generally being the largest heat source for a river or stream (Morin and Couillard, 1990; Webb and Zhang,1997, 2004).
Incident shortwave radiation (Hsw) from the sun is typically the largest source of energy for a river system (particularly during summer months; Webb and Zhang, 1997), although bankside objects such as vegetation and/or topography can reduce the amount of solar radiation received by the river through providing shade (e.g. Garner et al., 2014, 2017).
Longwave radiation (Hlw) (Dugdale, 2016) can be both a heat source and sink, with downwelling longwave radiation from clouds, the land surface and bankside vegetation contributing to heat gains, and upwelling radiation from the water surface driving energy losses from the stream (e.g. Benyahya et al., 2012).
Outgoing longwave radiation (Hlw) from the river channel represents a common heat sink, especially during night time or the winter months but incoming longwave energy from the atmosphere (and riparian vegetation) can mediate heat losses in certain circumstances (Benyahya et al., 2012; Hannah et al., 2008).

Energy at the air-water interface is also gained or lost through non-radiative means (latent and sensible heat ﬂuxes; Hannah and Garner, 2015).
Latent heat ﬂux (He) comprises energy lost (gained) by the stream during evaporation (condensation) as water moves from a higher to lower energy state (or vice versa).
Latent (evaporative) heat loss is a signiﬁcant energy sink at the river surface (Webb and Zhang, 1997, 2004), particularly in large or open rivers (Maheu et al., 2014; Caissie, 2016).
Sensible heat ﬂux (Hs) encompasses mainly convective exchange between the air and water surface depending upon temperature diﬀerences and atmospheric mixing (Webb and Zhang, 1999). The magnitude of energy lost or gained through sensible heat exchange is generally lower than radiative or latent ﬂuxes (Caissie, 2006). However, sensible heat ﬂuxes can nonetheless impose a non-negligible control on river temperature (e.g. Webb and Zhang, 1997), acting as both a heat sink in the winter and a heat source during summer months.

While generally smaller in magnitude than surface heat ﬂuxes (Sinokrot and Stefan, 1994; Evans et al., 1998), energy exchange at the streambed-water interface has been noted an important component of the energy balance in some studies, particularly in the winter (e.g. Webb and Zhang, 1997; Hannah et al., 2004; Leach and Moore, 2014). At the water-streambed interface, heat is principally exchanged through advective (Ha) and conductive (Hbhf) processes.
Advective heat (Ha) transfers from groundwater exﬁltration and hyporheic exchanges drive both river temperature warming and cooling (e.g. Hannah et al., 2009; Hébert et al., 2011). Because the temperature of groundwater is broadly stable over the year and the water column exhibits a sinusoidal annual cycle, streambed advective exchanges contribute to stream cooling in the summer and warming during winter months (Caissie, 2006).
Conduction (Hbhf) between the water column and streambed also drives heat exchange. These ﬂuxes generally act in the same direction as advective transfers, with heat being, lost from the water column to the (comparatively) cooler bed in the summer (Webb and Zhang, 2004).
However, radiative (shortwave (Hsw)) heating of the bed in in shallow streams can also drive positive conductive transfers from the bed to the water column (e.g. Evans et al.,
1998).

A ﬁnal source of energy at the water-streambed interface is ﬂuid friction between the water column and bed/banks. Friction gains are generally minor (e.g. Evans et al., 1998) and often considered negligible (Carrivick et al., 2012) for most rivers, but are sometimes observed in energetic environments (i.e. mountainous streams) with high roughness coeﬃcients (Brown and Hannah, 2008) or large bed material (Chikita et al., 2010).
Heat gains from ﬂuid friction can be a signiﬁcant source of heat in steeper streams with high roughness coeﬃcients (e.g. Hannah et al., 2004; Chikita et al., 2010; Khamis et al., 2015).

Once net heat ﬂux has been calculated, the river temperature change resulting from this energy gain (loss) is computed using Eq. (2).
The literature contains many variations on this equation (e.g. Sinokrot and Stefan, 1993; Rutherford et al., 1997; Tung et al., 2006; Hébert et al., 2011; Garner et al., 2014) which attempt to account for variability in discharge and channel morphology or compute heat transport in multiple dimensions. However, the basic one-dimensional heat advection-dispersion equation for an open channel of constant cross section and ﬂow is given by Sinokrot and Stefan (1993) :
{∂T_w} over {∂t} = - U{∂T_w} over {∂x} + D_L{∂T_w^{2}} over {∂x^{2}} + {H_total} over {ρ * c_p*d} ` ` ` ` ` (2)

where Tw is water temperature (°C) at time t,
U is mean channel velocity (ms−1),
x is streamwise distance (m),
DL is an empirically derived longitudinal dispersion coeﬃcient (ms−2),
ρ is the density of water (kgm−3),
cp is the speciﬁc heat of water (41.8 × 103 Jkg−1 °C−1),
d is the mean channel depth (m)

Provided that the channel is well mixed and does not contain notable lateral temperature gradients, the combination of Eqs. (1) and (2) can be used to simulate water temperature as a function of the input hydrometeorological and geomorphological data.
All process-based river temperature models use observed hydrometeorological data to calculate the energy ﬂuxes detailed in Eq. (1). the numerical representation of the physical energy ﬂuxes can vary substantially between diﬀerent river temperature models, and has implications for both model complexity and the quality of river temperature simulations.

2- Representation of fluxes
Incoming solar shortwave radiation
If observations of solar radiation (Hsw) are available for a given location, most models allow for the direct input of such data. Many process-based river temperature models contain complex routines capable of approximating the solar radiation received by a given point on the Earth's surface as a function of the date and time (see Boyd and Kasper, 2003 for appropriate algorithms). Because such algorithms yield predictions of solar radiation uninﬂuenced by the atmosphere, these models include further functions allowing for solar radiation values to be corrected for atmospheric transmissivity resulting from a range of factors (e.g. cloudcover, atmospheric dust/water vapour scattering, see Theurer et al.,1984 and Boyd and Kasper, 2003 for more detailed summary). Certain models even oﬀer the facility to use both observed solar radiation values and computed data.

Net longwave radiation
Some studies involving process-based river temperature models (e.g. Garner et al., 2014) incorporate observations of longwave radiation (Hlw) acquired from net radiometers, but such data are rarely available. all of the river temperature models summarised in Table1 oﬀer the ability to compute longwave radiative ﬂuxes as a function of other meteorological variables using a variant of the equation :

H_lw = H_(lw atm) - H_(lw stream) ` ` ` ` ` (3)

H_(lw atm) = (1 – R_L)* %epsilon_atm*%sigma*T_a ^4 ` ` ` ` ` (4) H_(lw stream) = %epsilon_w *%sigma* T_w^4 ` ` ` ` ` (5) given and

where εatm and εw (≈0.97) are the emissivity of the stream and the atmosphere respectively,
RL is the reﬂectance coeﬃcient of the stream surface (given as 1 − εw),
σ is the Stefan-Boltzmann constant (5.670367 × 10−8 Wm−2K−4),
Ta and Tw are the air and water temperature (°K) respectively

Complexities arise from the range of diﬀerent formulae available for the calculation of εatm. Most models calculate εatm as a function of either air temperature (Swinbank, 1963; Idso and Jackson, 1969) or vapour pressure (Brunt, 1932; Anderson, 1954) using simple empirically derived formulae, while others use the physically derived method of Brutsaert (1975) to compute εatm as a function of both air temperature and vapour pressure.
Some models even oﬀer multiple or composite methods for characterising εatm.
Additionally, because atmospheric emissivity is heavily inﬂuenced by cloud cover, a number of models oﬀer the ability to correct computed emissivity values for the eﬀect of cloud cover using the approach of Bolz (1949), something that is particularly useful in regions where cloudy/overcast conditions dominate.
Particular care should be taken when attempting to apply a river temperature model in environments with potential for a high proportion of longwave ﬂuxes (e.g. those with substantial tree/vegetation cover, or cloud-dominated meteorology); in such instances, it may be advisable to quantify incoming radiative energy (e.g. Hannah et al., 2008) using net radiometers.

Accounting for the eﬀects of riparian vegetation/topography on radiative ﬂuxes
It is necessary to account for the eﬀect of trees and topographic shading on radiative ﬂuxes when modelling stream temperature in such environments with near-stream vegetation and topography. While some models do not contain any mechanism to account for the eﬀect of vegetation/topography on radiation ﬂuxes, most incorporate algorithms that are able to simulate the reduction in solar shortwave radiation received by the stream.
Some models compute the eﬀects of shading using (amongst other variables) sun elevation, tree/topographic height and bank distance, canopy density and stream azimuth to compute a ‘shade factor’ coeﬃcient that represents the fraction of radiation that does not reach the stream surface due to shading. This coeﬃcient can then be applied to scale the solar radiation components of Eq. (1).
Other more complex algorithms function similarly, but partition incoming solar radiation into its direct and diﬀuse components. The direct solar radiation received at the stream surface is subsequently calculated either through application of the ‘shade factor’ coeﬃcient or through modelling the amount by which the solar ‘beam’ is attenuated as it travels through the tree canopy. The fraction of diﬀuse radiation received by the stream is then quantiﬁed separately, usually by means of an algorithm that computes the reach's sky view factor, a coeﬃcient that represents the fraction of the hemisphere that is unblocked by tree cover/topography. Most shading algorithms are directly integrated within their given stream temperature model. However, some models require that the shading correction be computed externally. Generally, these models rely on GIS analysis or similar to compute either the shade factor coeﬃcients or canopy transmissivity values which are then entered manually into the model. Although this additional step may mean that such models require more time to implement, the ability to manually enter shade correction values means that they are :
a) able to make use of advances in new shade correction algorithms
b) can be used with ﬁeld-derived values for shade correction (e.g. Rutherford et al., 1997) that do not rely on the application of an algorithm.

Some models also apply shading correction to longwave ﬂuxes. Atmospheric longwave radiation is aﬀected by riparian/topographic shading in much the same as the diﬀuse component of solar radiation ﬂux (Hannah et al., 2008). As such, the impact of shading on the atmospheric longwave ﬂux is generally calculated by computing a given reach's sky view factor (e.g. Cox and Bolte, 2007) and applying the resulting coeﬃcient to scale the longwave ﬂux given by Eq. (4).
Radiation from near-stream vegetation or topography can also represent a signiﬁcant source of longwave energy. Indeed, studies show that longwave radiation from tree cover can contribute signiﬁcantly to river temperature during nighttime (in comparison to open reaches; Benyahya et al., 2012; Hannah et al., 2008). As a result, the same models also contain routines that compute incident longwave radiation from riparian tree cover and/or topography. This allows such models to estimate longwave radiation ﬂuxes in tree-covered reaches with a high degree of accuracy, potentially improving their utility for predicting water temperature in steep headwater streams or heavily forested catchments.

An additional consideration concerns the spatial discretisation of the computed impacts of riparian vegetation on stream temperature. Because riparian vegetation can vary substantially along a river, any correction for riparian shading or longwave ﬂuxes must account for spatial variability in riparian vegetation. All of the models reviewed here contain routines capable of generating such spatially explicit data using either GIS polygons, tree height rasters or shading coeﬃcients as input data to correct radiative ﬂuxes at the scale of the model's structure (see Section 4.3). However, it is important that the chosen model's resolution is suﬃciently high to encapsulate true spatial variability in the impacts of riparian vegetation on stream temperature. Similarly, the riparian vegetation data provided to the model must be of a resolution equal to or better than that of the model itself. Recent studies have demonstrated the utility of LiDAR data for providing high resolution raster datasets of riparian vegetation height/shading (e.g. Wawrzyniak et al., 2017); such data are therefore particularly appropriate if attempting to model the ﬁne-scale (i.e. sub-reach) impacts of vegetation on stream temperature.

Latent and sensible heat ﬂuxes
Because direct measurements of energy gains or losses from latent or sensible heat ﬂuxes are rare (Maheu et al., 2014; Caissie, 2016), all of the river temperature models reviewed here derive net latent and sensible heat from meteorological observations.
The majority of equations for calculating latent heat ﬂuxes take the same initial form :
H_e = ρW*L_e* overline {E} ` ` ` ` ` (6)
where ρW is the density of water (1 × 10 kgm),
Le is the latent heat of vaporisation (2.5 × 106 Jkg−1),
Ē is the rate of evaporation (ms−1)

However, diﬀerences in computed latent heat ﬂuxes arise from the choice of equation used to compute Ē (Table 3). While some models currently oﬀer only relatively basic functionality for predicting evaporation rates as a function of air temperature and number of daylight hours (using the Thornthwaite, 1948 formula), the majority use a variation on Dalton's equation for evaporation (see Lim et al., 2012) to compute evaporation rates using wind speed, actual vapour pressure and saturation vapour pressure.
Most equations based around Dalton's equation involve some kind of empirical expression that estimates the adiabatic portion of evaporation as a function of wind speed and ﬁeld-derived coeﬃcients (referred to as the ‘wind function’, common coeﬃcients for which can be found in Boyd and Kasper, 2003 and Cole and Wells, 2015. The accuracy of eva- poration predictions can thus depend greatly upon the coeﬃcients used.
In an attempt to reduce the uncertainty associated with such empirical approaches, other models oﬀer the ability to use physically based equations (e.g. Penman, 1948; Monteith, 1965; Priestly and Taylor, 1972) that calculate evaporation rates based on a range of input hydrometeorological data (e.g. net irradiance, wind speed, saturation vapour pressure curve, aerodynamic conductance). The use of a model that incorporates a physically-based evaporation routine may be advisable when implementing a river temperature model in an environment for which ‘wind function’ coeﬃcients needed by Dalton-type approaches are unavailable. However, comparative studies present conﬂicting results regarding the relative accuracy of the various methods for computing evaporation (e.g. McJannet et al., 2013; Ouellet et al., 2014b; Alazard et al., 2015) meaning that is may not be advisable to apply these more complex routines unless evaporation rates predicted by simpler methods (e.g. Dalton's equation) are clearly erroneous.
Paragraphe bizarre
Conversely, while evaporative ﬂuxes are generally of greater magnitude in warmer climates, they can represent a highly signiﬁcant component of stream energy budgets in temperate regions (e.g. Hannah et al., 2008). It may therefore be advisable to measure the importance of evaporative ﬂux using an energy balance study (e.g. Hannah et al., 2008) or evaporation pan experiments (e.g. Maheu et al., 2014) prior to determining whether to apply a model with more complex routines for computing latent heat ﬂux.

All of the models reviewed here calculate sensible heat exchanges in essentially the same way following the method of Bowen (1926), either through multiplying the product of the wind function and the air-water temperature gradient by an empirical coeﬃcient, or by applying the Bowen ratio (itself a function of air and water temperature and vapour pressure) to the evaporative ﬂux. Consultation of the literature for the various temperature models documented here reveals minor discrepancies between the various sensible heat ﬂux equations and coefﬁcients used therein, largely resulting from either unit conversions and/or the necessity of accounting for diﬀerent wind function coeﬃcients. There is consequently little eﬀective diﬀerence in sensible heat ﬂux estimates yielded by the various models discussed here, meaning that model selection is generally driven by other (greater magnitude) sources of thermal energy (e.g. radiative, latent and advective ﬂuxes).

Heat ﬂuxes at the streambed interface
Some river temperature models do not incorporate routines capable of calculating bed heat ﬂux, considering its eﬀect on water temperature to be negligible. This is presumably because the majority of these models are designed for application in large river systems where the magnitude of heat exchanges at the streambed interface is particularly diminished in relation to other ﬂuxes (Caissie et al., 2014). However, many other models do incorporate bed heat ﬂuxes into their energy balance computations. This is generally accomplished using a variation on Fourier's Law (e.g. Story et al., 2003) whereby bed heat ﬂux is computed as a function of the streambed thermal gradient (change in temperature between the streambed-water interface and a given depth within the streambed; Theurer et al., 1984) multiplied by the bed thermal conductivity (the product of bed sediment density, bed heat capacity and bed thermal diﬀusivity; Boyd and Kasper, 2003). Most of these models refer to this equation as quantifying heat ﬂux arising from conduction between the bed and the water column. However, Hannah et al. (2004) note that it is extremely diﬃcult to disaggregate bed conduction, convection and advection when estimating bed heat ﬂux. Bed heat ﬂux computed with this method may therefore be considered a combination of these three energy exchanges.
As with other heat ﬂuxes detailed here, the quality of bed heat ﬂux predictions is reliant on input data quality and availability. Bed temperature gradient is generally measured using temperature loggers installed at given depths within the bed or modelled numerically given a priori knowledge of the bed material and temperature gradients within the riverbed (e.g. Sinokrot and Stefan, 1993), while thermal conductivity is governed by the type of bed material (i.e. lithology, porosity) and derived from laboratory analysis of bed sediments (data for which are often available in the literature; Hondzo and Stefan, 1994).
Observations of these parameters can be diﬃcult to ascertain, and it is often necessary to provide estimates to the temperature model. However, owing to the high degree of heterogeneity often present in bed temperatures (e.g. Birkel et al., 2016), obtaining even an average or estimate can be diﬃcult. In such circumstances, care must be taken to ensure that modelled bed heat ﬂuxes stay within realistic values. Furthermore, given the importance of conductive and advective (e.g. hyporheic-driven) bed heat ﬂuxes in some regions (e.g. Leach and Moore, 2014), the use of such ‘bulk’ approaches for computing bed heat ﬂuxes produces a highly simpliﬁed estimate of true bed energy transfer processes. Although recent research (e.g. Kurylyk et al., 2016; Caissie and Luce, 2017) has proposed improved methods for quantiﬁcation of bed heat ﬂuxes (and subsequent partitioning into their conductive, convective and advective components), these approaches have not yet been integrated into existing river temperature models and accurate modelling of bed heat ﬂuxes therefore remains a challenge.
In addition to the calculation of ‘bulk’ bed heat ﬂuxes, some models also include separate routines capable of estimating heat ﬂux due to solar heating of the bed. In most cases, river temperature models function under the assumption that the channel is deep enough that all solar radiation is attenuated within the water column. However, in certain circumstances (i.e. shallow headwater streams, streams with considerable exposed boulder material, very low turbidity environments; Chen et al., 1998a), solar warming of the streambed may contribute signiﬁcantly to river temperature warming (e.g. Evans et al., 1998; Clark et al., 1999; Webb and Zhang, 1999; Johnson, 2004). Because the magnitude of such heat ﬂuxes is both temporally or spatially variable (Webb and Zhang, 1997), it may be beneﬁcial to choose a model that accounts for these processes when modelling temperature in environments where radiative streambed warming is thought to occur. Where possible, it is therefore advisable to quantify the magnitude of bed heat ﬂuxes either by means of Fourier's law (e.g. Story et al., 2003) or by using soil heat ﬂux plates, in order to determine whether
a) the use of a model capable of accounting for bed heat ﬂuxes is necessary
b) the extent to which modelled ﬂuxes approximate observed data

Fluid friction with the bed and banks
Although only two publicly available models currently include routines for calculating ﬂuid friction, a range of studies have used the same simple equation for manually estimating friction-driven heat ﬂuxes (e.g. Marsh, 1990; Webb and Zhang, 1997; Hannah et al., 2004; Tung et al., 2006; Chikita et al., 2010; Cardenas et al., 2014). Should suspicions arise that the non-accounting for ﬂuid friction by a given model is biasing temperature estimates (e.g. in the case where the user is conﬁdent that all other heat ﬂux parameters are accurately modelled but temperature simulations still do not match observed data), it should at least be possible to estimate friction gains/losses outside of the model.
Furthermore, many coupled hydraulic-water temperature models already include routines for quantifying ﬂuid friction as part of their hydraulic computations. Given the ready ability to customise/script these models, it may be possible to devise routines which use the outputs of these computations to improve temperature estimates in high gradient streams. Nevertheless, with the exception of a few studies (e.g. Webb and Zhang, 1997, 1999) where ﬂuid friction was estimated to be high, such heat exchanges are generally assumed to be minor and can be considered negligible for the majority of temperature modelling scenarios (e.g. Carrivick et al., 2012; Johnson et al., 2014). The ability of a model to account for ﬂuid friction can therefore be considered a low priority during model selection, unless working in particularly high-energy environments.

Advective heat ﬂuxes
Inﬂows from tributaries or subsurface inputs can engender substantial temperature gradients in river systems (e.g. Torgersen et al., 1999; Torgersen et al., 2001). All of the models covered in this review contain routines capable of computing advective heat ﬂuxes using the same general equation:
T_(w,x) = {(T_(w,x−1) * Q) + (T_inflow * Q_inflow )} over {Q + Q_inflow} ` ` ` ` ` (7)

where Q and Qinflow are the discharge of the main channel and inﬂow respectively and Tinflow is the temperature of the inﬂow (Boyd and Kasper, 2003)
However, diﬀerences between the various models arise from :
a) the way in which boundary conditions are assigned to advective inputs,
b) the way in which inﬂows arriving from diﬀerent sources are disaggregated
c) the resolution at which inﬂows can be assigned within the model

In terms of assigning boundary conditions to advective inputs, the majority of temperature models require the user to manually input discharge and temperature data associated with inﬂows. These observations are relatively easy to obtain for surface inﬂows by means of temperature loggers and discharge gauges. Subsurface inputs are harder to quantify, given the scarcity of groundwater temperature records in many locations and the diﬃculty of quantifying groundwater ﬂux.
Groundwater temperature is therefore often assigned a value equal to mean annual air temperature given the close correlation between these two variables (e.g. Karanth, 1987). However, in regions where groundwater temperature departs signiﬁcantly from this trend, advective heat ﬂuxes resulting from groundwater inﬂows may be over- or under-represented. The need for ﬂow or temperature observations can be minimised by using coupled hydraulic or hydrological models (see Sections 4.1 and 4.2) which are able to estimate the ﬂows and temperatures associated with advective inputs. However, although these models are able to simulate surface water contributions with a reasonable degree of accuracy, the resolution of simulated groundwater inﬂows is often extremely course, requiring additional data on groundwater exﬁltration/temperature to be manually entered.

In terms of the disaggregation of inﬂows resulting from diﬀerent sources, some models discriminate between tributary inﬂows and those arising from groundwater processes, allowing tributary inﬂows to be assigned as point inputs, with groundwater inﬂows (or indeed, losses to the aquifer; Boyd and Kasper, 2003) modelled as diﬀuse inputs distributed along a given reach. Because inﬂows from diﬀerent subsurface zones (i.e. hyporheic vs. shallow ground water) have varying hydrologic characteristics (i.e. groundwater ﬂux generally involves a permanent change in water volume whereas hyporheic ﬂux is characterised by recurrent exchanges to and from the bed over shorter distances and time periods), some models even oﬀer the ability to model thermal inputs from diﬀerent subsurface zones (i.e. saturated vs unsaturated zones; hyporheic ﬂow). However, other models require input of ‘bulk’ inﬂows at discrete intervals within the model which merge surface and groundwater inputs together. This means that the true location of a given inﬂow may not be accurately represented within the model as the ‘merging’ of several inﬂows will require that their input location is also a reﬂection of their combined values. Because subsurface inﬂows are often more diﬀuse than tributaries, the merging of advective inputs in this manner may result in a river temperature response that is not properly representative of true subsurface or surface water mixing processes (Pike et al., 2013). Assigning temperatures to these combined inﬂow data can be diﬃcult given the likely temperature diﬀerence between surface and subsurface inﬂows owing to their diﬀerent thermal characteristics. In such instances, it may therefore be advisable to apply Eq. (6) to estimate the bulk temperature of the combined inﬂows before it is input into the model.
However, it should be noted that through merging diﬀuse and discrete advective inputs in this manner, a model may produce a false representation of the location and magnitude of warm or cool water inputs which may have implications for certain studies focusing on such phenomena (e.g. the ecological signiﬁcance of cool water refuges; Dugdale et al., 2016). The ability of a river temperature model to represent advective ﬂuxes is also dependent upon its resolution and structure (covered in further detail in Section 4.3). While less of an issue for models using a high resolution gridded structure whereby inﬂows can be assigned to each grid cell (allowing for multiple advective inputs in a relatively small spatial scale), models operating at reach scales only allow for inﬂows to be assigned at the resolution of nodes/segments. An appropriate segment resolution must be chosen in order to ensure that the river temperature response to local advective inputs is represented in the correct geographic location in order that modelled temperature accurate reﬂects observed data when conducting model calibration.

3- Model implementation
The diﬀerences between the available temperature models are not limited simply to their representation of physical energy ﬂuxes there is also substantial variability in the ways in which the various models are implemented. These diﬀerences lie in their ability to model hydraulic (i.e. ﬂow velocity and wetted cross-section) and/or hydrological (i.e. discharge or rainfall-runoﬀ) data, their structure (i.e. their spatio-temporal resolution and dimensionality), considerations regarding their calibration, and the degree to which the models are publicly available and/or open to customisation.

Hydraulic data
As accurate temperature predictions require a good representation
of channel morphology, it is important to consider the methodology
that a given temperature model uses to obtain these parameters. At the
most basic level, a river temperature model requires input data con-
cerning the area and time over which energy transfers occur (e.g.
Theurer et al., 1984) in order to calculate total heat ﬂux for a given
section of river. Values of channel width, depth, and velocity for each
element within a model must be available in order to compute Eq. (2).
While these data are generally derived from ﬁeld measurements or GIS
databases, one of the principal limitations of stream temperature
models that require these data is their assumption that channel width,
depth and velocity remain temporally stable. In reality, variations in
discharge will inherently lead to changes in wetted cross-section and
ﬂow velocity, which will alter energy ﬂuxes at the channel surface and
bed. In ideal circumstances, time series of width, depth and velocity
change (obtained using dataloggers or similar) would enable the ap-
propriate values to be input into the model at each timestep, but such
data (especially spatially distributed observations) are rarely available
in practise. Instead, some temperature models have a limited ability to
account for changes in wetted cross-section and/or velocity either
through the use of Manning's equation (e.g. Robert, 2003) to compute
changes in width/depth as a function of stream gradient and velocity
(e.g. 21) or by using empirically derived discharge-width and dis-
charge-velocity ratings curves (e.g. 13, 17). However, given that these
methods rely on empirical or semi-empirical functions, the temperatures predicted by such models may only hold true in relatively
steady-state environments where there is little spatio-temporal change
in channel morphology or ﬂow velocity.
In an attempt to address these limitations, many river temperature
models are now coupled to hydraulic models (Table 7), allowing them
to simulate ﬂow velocity and wetted cross-section as a function of input
channel morphology data for the entire range of discharges exhibited
by the river (2, 5, 6, 9, 10, 12, 14, 18, 20). The ability to incorporate
spatially and temporally explicit hydraulic data into the temperature
model means that such models are able to calculate energy ﬂuxes in
more dynamic ﬂuvial environments with a greater degree of accuracy,
improving temperature predictions. However, such models are ne-
cessarily more complex, and their increased data requirements and
higher parameterisation may mean that their use is beyond the scope of
some river temperature studies. Additionally, the hydraulic model's
velocity/stage predictions must also be thoroughly calibrated/validated
against observed data, meaning that the implementation of such models
can be time consuming when compared to more simplistic systems.
Nevertheless, when working in environments that are particularly dy-
namic and/or prone to rapid changes in width/depth ratio which could
greatly impact stream temperature (e.g. upland environments), the se-
lection of a hydraulically-coupled model may be advisable.

Hydrological model
In addition to hydraulic functionality, other river temperature
models oﬀer full hydrological coupling, enabling the simulation of
discharge (as a function of input meteorology data) in addition to
temperature (Table 7). Such models are useful for simulating river
temperature in remote or sparsely gauged watersheds where hydro-
metric data are rare. Additionally, these models often allow for the
representation of diﬀerent thermal characteristics of multiple source
water components, oﬀering a high degree of utility for assessing the
consequences of changing hydroclimatic conditions on stream tem-
perature across watersheds with varying patterns of recharge and dis-
charge. However, the prediction of water temperature is often not the prime function of such models. Indeed, of the coupled temperature-
hydrological models detailed here, two were ﬁrst conceived as hydro-
logical models, with water temperature routines being added at a later
date (3, 15), while (5) and (10) are principally hydraulic/hydro-
dynamic models which also oﬀer routines for rainfall-runoﬀ and water
temperature simulation. This does not necessarily mean that tempera-
ture simulations from such models will be of lower accuracy than
dedicated river temperature models. However, model implementation
is generally more complex and the data requirements greater than
dedicated water temperature models. Nevertheless, because coupled
temperature-hydrological models allow for the simultaneous simulation
of discharge and temperature, they oﬀer increased utility with regards
to predicting the eﬀects of climate change to river ecosystems (e.g.
Danner et al., 2012; van Vliet et al., 2012; Ficklin et al., 2014), given
that climate change is expected to inﬂuence both of these metrics in the
future. The use of a coupled temperature-hydrological model may
therefore be advisable should the scope of a study extend to modelling
the impacts of future climatic warming on river ecosystems or should
temperature predictions be required for a river that lacks discharge
measurements. However, the hydrological model's discharge simula-
tions must be thoroughly calibrated/validated prior to use, a process
which can be time consuming. This, coupled with the relative com-
plexity of hydrological model implementation means that such models
will generally be unnecessary for most ‘conventional’ stream temperature studies

Spatial resolution
The spatio-temporal resolution of river temperature simulations
varies substantially between the various models discussed here (Fig. 3).
While some models are limited to providing temperature predictions at
relatively coarse scales and time steps, others eﬀectively oﬀer no upper
limit on resolution, allowing temperature predictions to be discretised
at a scale of the user's choosing. In terms of spatial resolution, model
choice is largely informed by the intended application. Models capable
of providing data at ﬁne spatial scales oﬀer increased utility to under-
standing linkages between ecosystem dynamics and water temperature
(through the use of models to locate cool or warm water refuges or
determine the ﬁne-scale response of stream temperature to vegetation),
while lower resolution models may be more relevant for providing sy-
noptic data to inform water resources management. In examining their
spatial resolution, river temperature models can generally be separated
into two classes: one-dimensional models, and multi-dimensional
(gridded) models (Table 7).
In one-dimensional models (1, 3, 4, 6–13, 15–19, 21), the river
channel is generally discretised as a series of segments or nodes of es-
sentially homogeneous conditions whose length is dependent on the requirements of the study and/or the presence of longitudinal dis-
continuities (e.g. tributary inﬂows, substantial changes in channel
morphology). Hydrometeorological data necessary for computing Eq.
(1) are attributed to each segment/node. Because meteorological ob-
servations are rarely discretised at the resolution of each segment/node,
meteorological data are either attributed to each model segment/node
manually (4, 6, 10, 12, 15–18) or by interpolation from one or more
nearby weather stations (3, 7, 9, 21). Channel morphology and hy-
drometric data necessary for computing Eq. (2) are also attributed to
each node or segment; in the case of 1D coupled hydraulic-temperature
models (6, 9, 10, 12, 18) nodes are assigned detailed measurements of
channel cross-section required by the hydraulic computations. Where
applicable, measurements of riparian vegetation necessary for the
shading routines of the model are also attributed to each segment/node.
Eqs. (1) and (2) are subsequently computed for each segment/node,
yielding temperature simulations in a single (longitudinal) dimension.
The longitudinal resolution of simulated temperatures is thus depen-
dent upon either the length of the segments or the spacing between
model nodes, and is generally a user-deﬁned property. In theory, this
means that such models should allow for predictions at extremely ﬁne
spatial resolution where required. However, in practise, the resolution
of temperature predictions is driven largely by the resolution of the
input channel morphology and hydrometeorological data. While in-
terpolation can be used to increase the resolution of input data allowing
for ﬁner scale simulations, the memory and processing/programming
limitations of the model may prohibit the use of very high resolutions.
Although some one dimensional temperature models focus on providing
simulations for single thread channels (4, 8, 11, 17), most also allow for
the computation of river temperature across entire networks, through
representing the river network as a directed graph (1, 3, 6, 7, 9, 10, 12,
13, 15, 16, 18, 19, 21). Such models are particularly useful for pro-
viding basin-wide predictions of water temperature, should such in-
formation be needed for management purposes or similar.
Gridded models (2, 5, 14, 20) allow for the simulation of tem-
perature in multiple dimensions. This facility is often unnecessary in
smaller rivers but such models are useful in larger systems where sig-
niﬁcant vertical and/or lateral temperature gradients exist such as
impounded rivers with deep stratiﬁed channels and reservoirs (e.g.
Wang and Martin, 1991; Hanna et al., 1999) or large rivers/estuarine environments (e.g. Ouellet et al., 2014a). Gridded models function in
the same general manner as 1D models using Eqs. (1) and (2). However,
Eq. (2) also computes advection/dispersion in multiple dimensions and
is necessarily more complex. Furthermore, because most gridded tem-
perature models are based on hydraulic/hydrodynamic models, tem-
perature simulations are provided at the same resolution as the
bathymetric grid used for hydraulic simulations (e.g. Deltares, 2014).
While this means that temperature predictions from gridded models can
be of a higher resolution than their 1D counterparts, input hydro-
meteorological data used in Eq. (1) are generally interpolated up to the
resolution of the model grid. Therefore, despite the higher spatial re-
solution, the accuracy of temperature predictions is largely dependent
on the quality of the interpolation, and may not be better than 1D si-
mulations. Furthermore, at particularly ﬁne resolution, the extremely
small modelled temperature diﬀerences between successive grid cells
may indeed be smaller than the error of the model itself. In light of this
and the fact that 2D and 3D river temperature models are generally
more complex to implement than simpler 1D models (and have sub-
stantially increased processing requirements), the additional function-
ality of gridded models may be redundant unless a study speciﬁcally
requires the ability to simulate water temperature in multiple dimen-
sions (e.g. in the presence of signiﬁcant stratiﬁcation or highly variable
turbulence/mixing patterns).

Temporal resolution
Temporal resolution is also an important consideration when
choosing a river temperature model. While some applications (i.e.
stream thermal regime classiﬁcation) require only simple daily metrics
(e.g. mean/maximum temperature) generated by models operating at
low temporal resolution, higher frequency data are often important.
Indeed, models operating at higher temporal resolution are able to
generate more advanced thermal metrics (e.g. period of time spent
above a given threshold), which can be useful for detailed studies of
stream thermal ecology or for informing river management decisions.
The diﬀerence between models in terms of their temporal resolution
is considerably more limited than in terms of their spatial resolution
(Table 7). The lowest temporal resolution models reviewed here (4, 17,
20) provide temperature simulations on a daily timestep, allowing for
broad characterisation of river temperature metrics. However, the
majority of models oﬀer considerably shorter timesteps, simulating
temperature on hourly or sub-hourly steps (1, 4, 6, 8, 9, 11, 15, 17, 18)
or even oﬀering no eﬀective minimum temporal resolution (2, 5, 7, 10,
12–14, 20, 21). Such models are readily able to reproduce diurnal
temperature variability and allow for the extraction of key temperature
metrics relevant to ﬂuvial ecology or water quality studies. However,
similar to that noted in Section 4.3.1, the minimum timestep of a model
is essentially governed by the temporal resolution of the input hydro-
meteorological data used to drive it, meaning that model choice should
be advised by both the requirements of the study and the available
discharge and meteorology observations. Given that model runtime is
intrinsically linked to the number of model timesteps (i.e. the length of
the simulation period divided by the temporal resolution), model se-
lection must be made with an appreciation of the processing time re-
quired to generate a temperature simulation.

Model availibility
Another key consideration when determining the most appropriate
river temperature model for a given study is the model's availability and
potential for customisation to a speciﬁc application (Table 1). Of the
models discussed in this paper, the majority are either publicly avail-
able (as of 2016) or have been made available at some point during
their development cycle. However, it is necessary to diﬀerentiate be-
tween models that are freely available to download (2, 5–7, 9, 11, 12,
15, 16, 19, 20) or on request from the authors (3, 17, 18, 21) and those
that are either proprietary (1, 14) or only available commercially (10).
Although some studies will require the additional functionality of
proprietary/commercial models (e.g. full hydrodynamic integration;
10, 14), the range of publicly available models that now exists means
that open-source/freeware alternatives are often the preferred option
for studies involving river temperature modelling. Additionally, the source code of many publicly available models is also available for
modiﬁcation (2, 3 5–7, 11, 12, 15, 16, 18, 20, 21), allowing the user to
edit the model routines and develop new modules as required. Such a
facility oﬀers increased ﬂexibility to a given temperature model, with
user-driven development of new functions allowing it to stay abreast of
advances in river temperature research. For example, the authors are
aware of at least one river temperature model where ready access to the
model's source code is driving user development of improved eva-
porative ﬂux and canopy shading functions (see St-Hilaire et al., 2015).

Model validation
Most river temperature models require calibration/validation to
ensure that they produce an accurate representation of true river tem-
perature. This is because models contain a simpliﬁed representation of
true energy ﬂuxes and basin physiography (see Section 3, 4.1–4.3),
meaning that simulations do not provide a perfect analogue of true
river temperature. In order to ensure that simulated temperatures are as
close to observed data as possible, the model must be calibrated by
tuning coeﬃcients related to the empirical elements of the heat budget
equations (see Ouellet et al., 2014b) or channel morphology (e.g. bed thermal conductivity, Manning's roughness) of the study river. De-
scriptive statistics are then used to quantify the relative performance of
the model against temperature observations recorded in-situ. Because
of the strong seasonal component present in river temperature series,
the use of the model's root mean-squared error (RMSE) is generally
preferred to the Nash-Sutcliﬀe model eﬃciency coeﬃcient (NSE; see
Janssen and Heuberger, 1995) or other similar measures due to the fact
that RMSE remains unbiased by seasonal cyclicity. Some river tem-
perature models are relatively highly parameterised, meaning that
model calibration can be laborious. In such cases, it may be advisable to
calibrate the model using algorithmic approaches (e.g. Zheng and
Wang, 1996; Hansen and Ostermeier, 2001; Arsenault et al., 2014) that
optimise model calibration by iteratively reﬁning parameters to mini-
mise the diﬀerence between observed and predicted values (i.e. by
minimising RMSE). However, when using such algorithms, care must be
taken to ensure that physically plausible bounds are used to constrain
the calibration coeﬃcients to ensure that the algorithm does not au-
tomatically arrive at a calibration which produces good temperature
simulations at the expense of unrealistic energy ﬂuxes. It may also be
advisable, when calibrating highly parameterised models, to conduct
sensitivity analyses to better understand how changes to the various
parameters inﬂuence model predictions. Such an exercise may help to
reveal not only important information regarding model functionality
and the inﬂuence of various parameters on simulated temperatures, but
may also infer the dominant processes controlling the thermal regime of
the modelled river.
In terms of data required for model calibration/validation, the vast
majority of studies involving river temperature modelling use tem-
perature loggers to provide observations of true water temperature.
Loggers are typically installed within the active channel and housed in
shielding to prevent bias from solar radiation and damage from colli-
sion with bedload. The spatial distribution and logging frequency
(temporal resolution) of temperature observations acquired using log-
gers is informed by the study and chosen model. While loggers are an
appropriate source of data for calibration/validation in most studies,
models operating at particularly ﬁne longitudinal scales may require
data at higher spatial resolutions. Indeed, spatially-continuous data
from ﬁbre-optic distributed temperature sensing (FO-DTS) technology
(e.g. Bond et al., 2015) or airborne thermal infrared (TIR) data (e.g.
Boyd and Kasper, 2003; Cristea and Burges, 2009) have been success-
fully used as data sources for river temperature model calibration/va-
lidation (models 6, 12). However, it should be noted that all three of
these methodologies (loggers, FO-DTS and airborne TIR) have limita-
tions; loggers in terms of their inability to provide spatially-continuous
data, FO-DTS in terms of the relatively short distance over which it can
be used and airborne TIR in terms of its ability to provide only a tem-
poral ‘snapshot’ of longitudinal river temperature variability. Where
possible, eﬀorts should therefore be made to combine these approaches
for achieving the best possible model calibration/validation.

4- Limitations and perspectives
Despite the generally high degree of accuracy with which modern
process-based temperature models are able to simulate thermal pro-
cesses in rivers (e.g. RMSE ≲ 1.0 °C at sub-hourly to hourly timesteps
over seasonal to annual periods; Garner et al., 2014; Hébert et al., 2015;
Woltemade and Hawkins, 2016), there remain several limitations to
their application. Primarily, these limitations relate to issues associated
with the energy balance calculations or input resolution (see Sections 3
and 4.3). In terms of energy balance, models are often limited by the
relative simplicity of their process representation. Surface ﬂuxes usually
dominate the energy budget (Caissie, 2006) and so models have focused
on quantifying surface heat transfers with a good degree of detail.
However, there is still room for improvement, particularly with regards
to modelling the impacts of riparian vegetation on heat ﬂuxes at the air-
water interface. While most models are now capable of computing the
impact of riparian tree cover on radiative ﬂuxes, none are currently able
to quantify how bankside vegetation alters turbulent heat ﬂuxes
through alterations to the riparian microclimate (e.g. Dugdale et al.,
2018). Improvements in this regard would aid model performance in
forested regions and help eﬀorts to understand future impacts of land-
use or climate change on river temperature regimes.
Energy ﬂuxes at the streambed interface are less well represented by
currently available models, and many provide only a relatively gen-
eralised ability to quantify bed heat ﬂuxes or advective heat transfer.
Because of this, modelling river temperature in systems with major
groundwater contributions requires special attention. The limited
ability of currently available models to represent heat and mass trans-
fers from diﬀerent sources (e.g. soil water, groundwater) coupled to the
lack of large-scale estimates of certain inﬂow types (e.g. hyporheic
ﬂow) is a major challenge, and future research should therefore focus
on improving model representation of subsurface ﬂuxes. The potential
coupling of river temperature models to detailed groundwater-surface
water ﬂux routines (e.g. Kurylyk et al., 2014) could help to address this
shortcoming, as could further research characterising the spatio-tem-
poral variability (and driving mechanisms) of hyporheic ﬂuxes (e.g.
Birkel et al., 2016). Such advances would help improve model perfor-
mance in groundwater dominated regions and also shed new light on
the role of subsurface hydrological processes in driving river tempera-
ture (a research gap noted by Hannah and Garner, 2015).
In addition to groundwater, the representation of energy advected
by other phenomena such as precipitation (e.g. Null et al., 2013) or
meltwater (e.g. Greene and Outcalt, 1985) is often omitted from the
energy balance. While these energy transfers are sometimes covered by
coupled hydrological-water temperature models (e.g. van Vliet et al.,
2012), more ‘unusual’ ﬂuxes such as heat generated through ﬂuid
viscosity (resulting from friction generated by the movement of water
molecules against each other) or energy contributions from in-stream
chemical and biological processes (Webb and Zhang, 1997) or pre-
cipitation are very rarely quantiﬁed. The development of model rou-
tines capable of computing these heat ﬂuxes would help to ‘close’ the
model's energy balance, minimising errors resulting from the non-re-
presentation of such ﬂuxes. Indeed, such data would reduce uncertainty
regarding whether model errors arise from the simplicity of the model's
heat budget or from other sources. Further research is therefore needed
into how best to implement these ‘unusual’ energy ﬂuxes within river temperature models and the circumstances where they may represent a
signiﬁcant source (sink) of energy. However, it is important to re-
member that in the majority of cases, the conventional energy balance
equation (Eq. (1)) produces a more-than-adequate representation of
heat ﬂuxes, and the addition of such extra layers of complexity is
generally unnecessary.
Another limitation of current process-based river temperature
models relates to the availability and resolution of input meteorological
and physiographic data. Because process-based models require input
meteorology or land-use data, their utility for modelling temperatures
in remote locations is limited. Furthermore, even when data does exist,
river temperature model inputs are often based on point data (i.e. single
isolated meteorological stations or coarse-resolution land-use data)
which are unable to encapsulate variability in hydrometeorology or
basin physiography. Diﬃculties in scaling up model inputs from these
point locations to the resolution of the chosen model can impact si-
mulation quality. There is consequently a need to develop approaches
for the acquisition and/or upscaling of data necessary for modelling
temperatures in inaccessible regions or at increased resolutions.
Geostatistical approaches have previously been used with success to
upscale meteorological data (e.g. air temperature; Spadavecchia and
Williams, 2009) and channel morphology (e.g. Legleiter and Kyriakidis,
2008; Merwade, 2009). However, neither of these approaches has been
applied in a river temperature modelling context, and more research is
therefore needed in order to facilitate the application of process-based
models in data-poor regions. Similarly, while remote sensing has shown
strong potential for deriving ﬁne scale observations of meteorology
(e.g. Rienecker et al., 2011; Vinukollu et al., 2011) and/or channel
morphology (e.g. Marcus and Fonstad, 2008; Fonstad et al., 2013) that
would be suitable as inputs to river temperature models, studies com-
bining these remote sensing approaches with river temperature mod-
elling are uncommon. Future research combining statistical upscaling
methods with remote sensing should thus be prioritised with a view to
generating high resolution meteorology and physiographic inputs ne-
cessary for improving river temperature model performance, particu-
larly in remote locations. Given that remote sensing has been demon-
strated useful both for deriving and providing ﬁne scale temperature
data needed for model calibration/validation (through the application
of thermal infrared imagery; Handcock et al., 2012), the combination of
river temperature models with remote sensing data (e.g. Vatland et al.,
2015) clearly has potential.
A ﬁnal limitation to the use of water temperature models concerns
the necessity of specifying boundary conditions to the model and the
implications of this for reach- to watershed-scale temperature models.
In all process-based water temperature models, water temperature is
both the product and a boundary condition of the energy balance be-
cause it is required for the calculation of outgoing longwave radiation,
turbulent heat ﬂuxes and bed heat ﬂux (see Sections 3.1.2, 3.2 and
3.3.1) which are in turn used to compute water temperature (Moore
et al., 2005). This means that data concerning water temperature are
actually required by the model to then simulate temperature. For small
reach-scale models with few advective inputs, a single upstream tem-
perature boundary condition may suﬃce. However, in the case of larger
models with multiple inﬂows, it is necessary to attribute a temperature
boundary condition to each of these inputs, meaning that additional
input river temperature observations are required. Unfortunately, this
can lead to considerable data requirements when modelling entire river
networks. The use of coupled hydrological-water temperature models
(which eﬀectively simulate river discharge and temperature from
source to conﬂuence; e.g. 3, 7, 15) may alleviate this problem, as only
the boundary condition required is the water temperature of the
headwater exﬁltration (which can be approximated by mean annual air
temperature; e.g. Karanth, 1987). Alternatively, spatial regression
models or spatial statistical network models (e.g. Jackson et al., 2017;
Isaak et al., 2015) could be used to provide boundary conditions at
locations for which temperature observations do not exist. However, it is necessary to note that composite model approaches such as these may
increase model error due to the multiple layers of uncertainty asso-
ciated with the simulated data.
In their review paper, Benyahya et al. (2007) noted the importance
of the newer generation of statistical models for understanding the in-
ﬂuence of environmental variables on stream temperature. We suggest
that process-based temperature models have an equally important role
to play in the river sciences and that the two approaches are highly
complementary. Because of process-based models' unique ability to il-
luminate the fundamental processes driving river temperature dy-
namics, they are ideally positioned to inform appropriate metrics to be
used in larger-scale statistical approaches. Conversely, statistical ap-
proaches provide a potential solution for addressing issues of data or
boundary condition availability within process-based models. There is
therefore substantial scope to combine statistical and process-based
models in a complementary capacity, not only to improve the quality of
river temperature simulations from existing models, but also to better
identify and understand the fundamental linkages between hydro-
meteorology, river basin properties, and river temperature. Such ad-
vances will allow for more accurate river temperature projections in
space and time, and will be of great use to water resource managers and
other environmental practitioners charged with better understanding
and protecting sensitive river environments. We hope that the in-
formation presented here spurs further investigations using process-
based river temperature models, in terms of both their continued re-
ﬁnement and their use for addressing fundamental questions in the
river sciences.

Liste des articles utilisés :
Alazard et al., 2015
Anderson, 1954
Benyahya et al., 2012
Birkel et al., 2016
Bolz (1949)
Bowen (1926)
Boyd and Kasper, 2003
Brown and Hannah, 2008
Brunt, 1932
Brutsaert (1975)
Caissie, 2006, 2014, 2016
Caissie and Luce, 2017
Carrivick et al., 2012
Cardenas et al., 2014
Chen et al., 1998a
Chikita et al., 2010
Chen et al., 1998a
Cole and Wells, 2015
Cox and Bolte, 2007
Dugdale et al., 2016
Dugdale, 2016
Evans et al., 1998
Garner et al., 2014, 2017
Hannah and Garner, 2015
Hannah et al., 2004, 2008, 2009
Hébert et al., 2011
Hondzo and Stefan, 1994
Idso and Jackson, 1969
Johnson, 2004
Karanth, 1987
Khamis et al., 2015
Kurylyk et al., 2016
Leach and Moore, 2014
Lim et al., 2012
Maheu et al., 2014
Marsh, 1990
McJannet et al., 2013
Monteith, 1965
Morin and Couillard, 1990
Ouellet et al., 2014b
Penman, 1948
Pike et al., 2013
Priestly and Taylor, 1972
Rutherford et al., 1997
Sinokrot and Stefan, 1993, 1994
Story et al., 2003
Swinbank, 1963
Theurer et al.,1984
Thornthwaite, 1948
Torgersen et al., 1999, 2001
Tung et al., 2006
Wawrzyniak et al., 2017
Webb and Zhang,1997, 1999, 2004

approches statistiques pour modéliser
https://peerj.com/articles/4894/
https://www.tandfonline.com/doi/full/10.1080/02626667.2014.914215

données RNT : bassin de la Loire couverture la plus homogène
La température des grands cours d’eau est essentiellement contrôlée par les conditions
atmosphériques ; La température des petits et moyens cours d’eau dépend des conditions géographiques et géomorphologiques de la station de mesure et du linéaire en amont de celle-ci ; en particulier, l’ombrage lié à la ripisylve et/ou les apports de nappe (pour les cours d’eau incisant un réservoir aquifère) peuvent contrôler la température de certains petits cours d’eau amont en jouant un rôle tampon par rapport aux variations de la température de l’air ; cet effet peut se propager d’amont en aval et doit être pris en compte pour comprendre la température de cours d’eau de taille moyenne ;

https://agupubs.onlinelibrary.wiley.com/doi/epdf/10.1029/2018WR023250